## Slide 1: Lesson 3 - EV3 Gyro Sensor
Csíkszereda RobotKlub 2024 - mARC NICHITIU - ??

## Slide 2: Curriculum
based on the Introduction to Programming EV3 Curriculum developed by Carnegie-Mellon Robotics Academy https://www.cmu.edu/roboticsacademy/roboticscurriculum/index.html
FLL City Shaper Challenge
              https://www.firstinspires.org/resource-library/fll/challenge/challenge-and-resources

## Slide 3: Main Goals for Today
Learn about the EV3 Gyro Sensor.
Learn about why we need the Gyro sensor to be precise in FLL.
Learn how to use the EV3 Gyro Sensor to stop at an angle.
Learn how to go straight with the EV3 Gyro Sensor.

## Slide 4: Gyro Sensor
❌
❌
❌
✅
The Gyro Sensor measures angles, and can thus measure a difference in angle.
For example, if the robot turns to the right 90°, the gyro would measure 90°.
The gyro can also measure angular speed.

## Slide 5: Gyro Sensor - Problems
❌
❌
❌
✅
The Gyro Sensor can sometimes lose precision over time.
It can also start to drift (increase/decrease value very fast without actual robot motion).
To solve these, we have a few hacks :)
First, lets turn for some angle.

## Slide 6: Turning for an Angle - Algorithm
❌
❌
❌
✅
Start the motors to spin the robot
  The robot is now turning
While the robot is turning, use the gyro sensor to check if the angle is big enough (turned enough)
When you hit the angle, stop !

## Slide 7: Gyro Sensor - Code
❌
❌
❌
✅
Structure:
  Initialize object/reference to Sensor:
    gyroSensor = GyroSensor(Port.S1)
  Obtain information: .speed(), .angle()
  We will not be using .speed() as it interferes with .angle().

## Slide 8: Gyro Sensor - Code - Example
❌
❌
❌
✅
If we wanted to find the gyro’s measured angle, we could write:
gyroSensor = GyroSensor(Port.S1)
ang = gyroSensor.angle()
print(ang)
We will try this in a minute.

## Slide 9: Turning for an Angle - Algorithm
❌
❌
❌
✅
Start the motors to spin the robot
  The robot is now turning
While the robot is turning, use the gyro sensor to check if the angle is big enough (turned enough)
When you hit the angle, stop !

## Slide 10: Gyro Sensor Program Tutorial
❌
❌
❌
✅
Start with initializing the gyro sensor, on port 1.
# Initialize Gyro Sensor
gyroS = GyroSensor(Port.S1)

## Slide 11: Gyro Sensor Program Tutorial
❌
❌
❌
✅
Now, initialize the DriveBase to control the robot’s movement.
# Initialize Gyro Sensor
gyroS = GyroSensor(Port.S1)
# Initialize motors
left_motor = Motor(Port.B)
right_motor = Motor(Port.C)
robot = DriveBase(left_motor,right_motor,wheel_diameter=55.5,axle_track=104)

## Slide 12: Gyro Sensor Program Tutorial
❌
❌
❌
✅
Add a command to tell the robot to start driving.
# Initialize Color Sensor
colorS = ColorSensor(Port.S3)
# Initialize motors
left_motor = Motor(Port.B)
right_motor = Motor(Port.C)
robot = DriveBase(left_motor,right_motor,wheel_diameter=55.5,axle_track=104)
robot.drive(0,45) # 0 forward speed, 45 deg/s turning (clockwise)

## Slide 13: Gyro Sensor Program Tutorial
❌
❌
❌
✅
Add the while loop. We check at each iteration whether the gyro sensor detected if we turned enough. If not, run the loop. If turned enough, stop. Inside the loop, place a time.sleep command to not abuse the robot computer. Don’t forget the import time command before the loop.
...
robot.drive(0,45) # 0 forward speed, 45 deg/s turning (clockwise)
import time
# while I have not yet turned 90°
while(gyroS.angle() < 90):
time.sleep(0.01)

## Slide 14: Gyro Sensor Program Tutorial
❌
❌
❌
✅
If the angle is reached, the loop exits. Thus, we tell the robot to stop driving.
...
robot.drive(0,45) # 0 forward speed, 45 deg/s turning (clockwise)
import time
# while I have not yet turned 90°
while(gyroS.angle() < 90):
time.sleep(0.01)
robot.drive(0,0)
robot.stop()
# end of program.

## Slide 15: Gyro Sensor Program Tutorial
❌
❌
❌
✅
#!/usr/bin/env pybricks-micropython
from pybricks.hubs import EV3Brick
from pybricks.ev3devices import (Motor, TouchSensor, ColorSensor,InfraredSensor, UltrasonicSensor, GyroSensor)
from pybricks.parameters import Port, Stop, Direction, Button, Color
from pybricks.tools import wait, StopWatch, DataLog
from pybricks.robotics import DriveBase
from pybricks.media.ev3dev import SoundFile, ImageFile
import time
# Create your objects here.
ev3 = EV3Brick()
# Initialize Color Sensor
gyroS = GyroSensor(Port.S1)
# Initialize motors
left_motor = Motor(Port.B)
right_motor = Motor(Port.C)
robot = DriveBase(left_motor,right_motor,wheel_diameter=55.5,axle_track=104)
robot.drive(0,45) # 0 forward speed, 45 deg/s turning (clockwise)
# while I have not yet turned 90°
while(gyroS.angle() < 90):
time.sleep(0.01)
robot.drive(0,0)
robot.stop()
# end of program.
Full Program:

## Slide 16: Lets test it
❌
❌
❌
✅
Run your program !!

## Slide 17: Problems
❌
❌
❌
✅
Question: What if my robot stops late ?
  Answer: Decrease the threshold of 90° to 87° or 85°, or lower the speed.
Question: What if my robot misses the angle ?
  Answer: Check that the gyro sensor is not drifting.

## Slide 18: Problems - Drifting Gyro - 1
❌
❌
❌
✅
If the gyro is drifting (changing value rapidly for no reason), we can do two things:
  We can recalibrate it by asking for a speed and then an angle:
  gyroS = GyroSensor(Port.S1)
  gyroS.speed()
  gyroS.angle()
  # done

## Slide 19: Problems - Drifting Gyro - 2
❌
❌
❌
✅
If the gyro is drifting (changing value rapidly for no reason), we can do two things:
  We can also tell the EV3 to ask for the wrong sensor, and then the correct one:
  try:
  tmp = UltrasonicSensor(Port.S1) # temporary wrong sensor
  tmp.distance() # asking for the wrong data
  except:
  print("failed")
  gyroS = GyroSensor(Port.S1)
  gyroS.angle()
  # done

## Slide 20: How is this useful ??
We have to go long distances on the field….

## Slide 21: How is this useful ??
If the robot moves straight, it shouldn’t change its angle right ?

## Slide 22: How is this useful ??
Lets follow an ‘angle’ across the table !

## Slide 23: Line Following - Gyro
Let’s remember from last time how we followed lines.
We followed the edge of the line, where the sensor read 50.

## Slide 24: Line Following - Gyro
This time, we’ll follow the actual imaginary line, where the gyro will always read the same thing.
We first store the initial value, and then follow that !

## Slide 25: Line Following - Algorithm - Boolean

## Slide 26: Line Following - Boolean
In python, we would have (after the initial part):
# Initialize Gyro Sensor
gyroS = GyroSensor(Port.S1)
robot.drive(250,0) # 250 mm/s speed, 0 turning (straight)
iniAng = gyroS.angle() # Initial heading
# while I have not yet covered my distance
while(robot.distance() < 200): # 200 mm = 20 cm
ang = gyroS.angle() # measure
  if(ang > 0): # to the right
  robot.drive(250,-20) # turn left
    else: # on black
      robot.drive(250,20) # turn right
time.sleep(0.01) # wait a little
robot.drive(0,0)
robot.stop()
# end of program.

## Slide 27: Line Following - Algorithm - Proportional
❌
❌
❌
✅
We can do better, just like for the colors !!
We can steer less if we are closer, and steer more if we are farther.

## Slide 28: Line Following - Algorithm - Proportional

## Slide 29: Line Following - Proportional
In python, we would have (after the initial part):
# Initialize Gyro Sensor
gyroS = GyroSensor(Port.S3)
robot.drive(250,0) # 250 mm/s speed, 0 turning (straight)
kP = 1 # Proportional Constant
iniAng = gyroS.angle() # Initial heading
# while I have not yet covered my distance
while(robot.distance() < 200): # 200 mm = 20 cm
ang = gyroS.angle() # measure
  err = iniAng-ang # positive error is to the left
      robot.drive(250, err*kP) # turn by err*kP
time.sleep(0.01) # wait a little
robot.drive(0,0)
robot.stop()
# end of program.

## Slide 30: Line Following - Algorithm - PD
❌
❌
❌
✅
We can still do better, just like for the colors !!
What if we changed direction slower ?
Derivative: change of some quantity over time
  Lets use it !

## Slide 31: Line Following - Algorithm - PD

## Slide 32: Line Following - PD
In python, we would have (after the initial part):
# Initialize Gyro Sensor
gyroS = GyroSensor(Port.S3)
robot.drive(250,0) # 250 mm/s speed, 0 turning (straight)
kP = 1 # Proportional Constant
kD = 0.1 # Derivative Constant
iniAng = gyroS.angle() # Initial heading
lastAng = iniAng
# while I have not yet covered my distance
while(robot.distance() < 200): # 200 mm = 20 cm
ang = gyroS.angle() # measure
aDiff = ang-lastAng # get difference
  err = iniAng-ang # positive error is to the left
      robot.drive(250, err*kP + aDiff*kD) # turn by err*kP
time.sleep(0.01) # wait a little
robot.drive(0,0)
robot.stop()
# end of program.

## Slide 33: Lets test it
❌
❌
❌
✅
Run your program !!

## Slide 34: Animation - kD = ‘D Gain’
❌
❌
❌
✅

## Slide 35: Problems
❌
❌
❌
✅
It doesn’t change anything :(
  Solution: increase kD!
It is too slow to correct for a bump in the path :(
  Solution: decrease kD!

## Slide 36: End
See you next time !
Never hesitate for questions.